Formal Methods for Partial Differential Equations
Francisco Penedo (franp@bu.edu)

---
Heat Equation
Temperature evolution (u(x,t)) on a 1D rod (Ω = (0, L)):
We denote this system by Σ.

---
LTL for PDEs
We include the spatial information in the atomic propositions
Informally,
Example:

---
Verification Problem
Given a system Σ, specification φ and initial region Θ ∈ 2Π check whether the trajectories of Σ satisfy φ for all initial values u0 ∈ [[Θ]]

---
Finite Element Analysis
Partition Ω into a finite set of “elements” with endpoints
Approximate the solution of Σ by interpolating the solution of
Where A and b are computed from the parameters of Σ. The A matrix is banded.
We call this system ΣFEM

---
LTL for FEM System
Only change atomic propositions:
Problem is now:
Given a system ΣFEM, specification φFEM and initial region Θ ∈ 2Π check whether the trajectories of ΣFEM satisfy φFEM for all initial values corresponding to u0 ∈ [[Θ]]
Issue: ΣFEM is an approximation! We need a priori error bounds

---
Transition System and Quotients
Usual approach:
- Partition state space of
- Compute quotient TS with respect to the partition
- Check satisfaction in the TS
Issue: is very high dimensional! (100 – 10000)
Idea: Make smaller quotients to check subformulas

---
TS and Quotients
For a formula in the form
We only need to check each individually.
Consider the full quotient TS, K, based on a rectangular partition of the state space:
And the equivalence relationships

---
TS and Quotients
We can check the satisfaction of a subformula using the quotient TS K/SI, where I contains all indices of di that appear in

---
Subsystems
How do we compute those quotients? Not from the full TS K, but from the subsystem corresponding to the equivalence relation:
The TS corresponding to this system is an overapproximation of the quotient K/SI
Regular
term
Polyhedral
disturbance

---
Example
Rod with L = 1000, g0 = 10, gL = 100. We want to check the spec with initial region
The FEM system for a norm 1 partition is given by the following matrices:

---
Example (cont)
A direct translation of the spec gives:
Each subformula has too many di, but we can rearrange it:
Now each subformula has only one di and we can check the corresponding quotient TS

---
Example (cont)
This TS doesn’t satisfy
All transitions are enabled!
Only trivial formulas will be satisfied for this TS
TS for d500 subsystem

---
STL for PDEs
Similar to LTL, we only need to define appropriate atomic propositions:
Example:

---
STL for FEM System
Same as LTL
In this formulation, we can translate the problem directly into a feasibility check for a Mixed Integer Linear Program

---
Example
Rod with L = 100, g0 = 10, gL = 100. We want to check the spec with initial value u0 = 20
The corresponding FEM system for a size 1 partition is similar to the previous example
We use Gurobi to check the feasibility of the MILP
It takes 437 seconds to solve the problem

---
Conclusions
- We can formulate verification problems for PDEs using temporal logics
- We can translate the problem into a verification problem for ODEs
- An abstraction based approach is not powerful enough for the high dimensional system
- MILP based approach is promising for extension to control problems
- A priori error bound still needed to connect PDE and ODE problems